## Slide 1: 7-GPU Architecture
Dr. Hamish Carr & Dr. Rafael Kuffner dos Anjos

## Slide 2: Agenda
How GPU’s work
Modern pipeline
Shaders

## Slide 3: GPUs
Can be discrete or integrated
Many levels, but all have custom silicon
  Hardware-software co-design
  For 35 years
COMP 5812M: Foundations of Modelling & Rendering
COMP 5812M: Foundations of Modelling & Rendering

## Slide 4: GPU-Centric PC Architecture
Core logic on motherboard
Everything fed to CPU
GPU connected over bus
  data transfer limited
  Batch transfer preferred
GPU often more powerful
  CPU is just the I/O processor

## Slide 5: High-Level View of GPU
Massively parallel by design
Many processors interacting
Shader
Core
Shader
Core
Shader
Core
Shader
Core
…
Interconnection network
Memory controller
Memory controller
Memory controller
…
Graphics RAM
Graphics RAM
Graphics RAM
…
(PC, Mask)
I-Cache
Decode
SIMD Execution
Scalar Pipeline
Scalar Pipeline
Scalar Pipeline
Scalar Pipeline

## Slide 6: GPU Characteristics
Many shader cores (1000s of processors)
Stream processing
SIMD using warps (NV) / wavefronts (AMD)
Small amounts of per-core memory
High latency to main VRAM
Stalling common when accessing data
But many 1000s of data to be processed
COMP 5812M: Foundations of Modelling & Rendering

## Slide 7: Context Switching
  A core computes something in register
  Then it accesses a texture and stalls
  So suspend the thread and start another
  And use hardware to perform the switch
  Return to first thread after data load done
  Minimises downtime, maximises throughput
  Because we have so many operations to do
COMP 5812M: Foundations of Modelling & Rendering

## Slide 8: SIMD Parallelism
Instructions shared between groups of cores
  Called warps (NVIDIA) / wavefronts (AMD)
  Usually 8-64 cores mapped to a SIMD lane
Works best with non-branching code
And when memory fetches are few
And when register usage is low
All this affects the occupancy rate
COMP 5812M: Foundations of Modelling & Rendering

## Slide 9: Simplified Example

## Slide 10: Divergence
If statements stall pipelines
Cores take different branches
Warp threads diverge
Branch to different codepaths
  Often controlled by semaphores
  Tends to cause bottlenecks
Branch
Path A
Path B

## Slide 11: The Modern Pipeline
Based on the projective rendering pipeline
With extra stages (of course!)
But essentially what we've been implementing
Fully
Programmable
Configurable
But Not
Programmable
Completely
Fixed Function
Required
Stage
Optional
Stage

## Slide 12: Terminology
Draw call – invocation by the programmer
Uniform input – value constant over draw call
Varying input – value varying per element
  Causes pipeline to execute & run shaders
  May involve 1000s of vertices

## Slide 13: Uniform vs. Varying
Uniform values are the same for all elements
E.g. lighting (i.e. a lot of OpenGL state)
Lots of constant registers available on GPU
Accessible from all cores
Varying values are different for each element
E.g. uv coordinates
Stored in local registers per core

## Slide 14: Unified VM Architecture

## Slide 15: Input Assembler
Fixed stage before vertex shader
Weaves together data streams
  E.g. mixing vertices & normal
  Striping data from vertex arrays
Also allows instancing
  Reuse of the same object multiple times
COMP 5812M: Foundations of Modelling & Rendering

## Slide 16: Vertex Shader
First stage under programmer control
Converts to clip space (required)
May also tweak vertex position, properties
Occurs before lighting computed
E.g. adjusting normal to generate a crease
COMP 5812M: Foundations of Modelling & Rendering

## Slide 17: Uses of Vertex Shaders
Deforming an existing mesh
Animation: skinning & morphing
Procedural deformation: flags, cloth, water
Particle creation: from degenerate meshes
Lens distortion, heat haze, &c.
Applying terrain height fields
COMP 5812M: Foundations of Modelling & Rendering

## Slide 18: Tessellation Stage
Allows converting mesh into finer mesh
Useful for higher-order surfaces
Saves memory / bandwidth
Consists of three internal stages
  Hull shader (tessellation control shader)
  Tessellator
  Domain shader (tessellation evaluation shader)
Zheng et al. 2020

## Slide 19: Tessellation Substages
Hull shader modifies input patch
Tessellator converts to smaller patches
Domain shader generates vertex attributes

## Slide 20: Geometry Shader
Converts primitives into other primitives
E.g. turns mesh into wireframe, point into quad
We will use this for a fur shader next term
Can be used to generate multiple streams
Not the most heavily used
  Because it is so general-purpose
  Means it is harder to optimise
COMP 5812M: Foundations of Modelling & Rendering

## Slide 21: Clipping, Mapping, Raster
Clipping stage trims off-screen portions
  Can convert triangle into quad (2 triangles)
Mapping stage is the viewport transform
Rasterisation we know about
  Generates fragments
  Computes barycentric coordinates
  Interpolates attributes from vertices
COMP 5812M: Foundations of Modelling & Rendering

## Slide 22: Pixel Shader
Also known as the fragment shader (OpenGL)
Input is fragments with attributes
Typically computes the fragment’s colour
  Also opacity, can modify z-depth
Has the ability to discard the fragment
Does not perform the depth test
Can render to multiple targets
COMP 5812M: Foundations of Modelling & Rendering

## Slide 23: Clipping in Pixel Shader
Input: nested spheres in different colours
  Already rasterised into fragments
  Discard any fragments in a known quadrant
  Simple geometric test on x,y,z

## Slide 24: Multiple Render Targets
We have used a colour and depth buffer
Why limit ourselves to two?
Pixel shader can write to many buffers
And can send output to different places
Eg: colour in one, object IDs in another
Leads to deferred shading
  Compute visibility, save attributes for later
COMP 5812M: Foundations of Modelling & Rendering

## Slide 25: Pixel Shader Limitation
Pixel shader can only write to its own x,y
Some exceptions in practice
However, different cores can have same x,y
Buffer locking done per-pixel in hardware!
Atomic operation means pixel shader stalls
But this is tolerable in practice, due to high number of fragments
COMP 5812M: Foundations of Modelling & Rendering

## Slide 26: Stream Output
Relax the constraint on pixel shader location
Allow it to write anywhere in a buffer
Which then just becomes an arbitrary array
Use the pixel shaders to compute anything
  Geometry, vertices, lighting, whatever
Then use the array as input in a second pass
  Multi-pass rendering & compute shaders

## Slide 27: Merging Stage
Output merger (DX) / Per-sample ops (OpenGL)
Combines individual fragments
  Essentially doing image processing
Includes depth-test, stencil-buffer, blending
In theory, can save and sort fragments (A-Buffer)
But in practice not common
COMP 5812M: Foundations of Modelling & Rendering

## Slide 28: Lighting
The vertex shader doesn’t do lighting
Because we now assume we do Phong shading
I.e. the pixel shader does it per-fragment
Before the z-test
We could test z in pixel shader (early-z: DX 11)
Or we can leave it to merging (DX 12)
  Why would we do it that way?
COMP 5812M: Foundations of Modelling & Rendering

## Slide 29: Deferred Shading
Don’t use all the attributes in the first pass
Just use the object ID & the uv coordinates
Framebuffer holds visible object IDs & uv
Now re-render a single quad
Only one fragment per pixel
Lighting computation only done once
Oosten 2015

## Slide 30: Net Result
The pipeline stages are malleable
We move computations around all the time
Do NOT assume that this will remain fixed
We may end up doing pure compute
  And leaving all of it up to the coder
  Until someone simplifies it again

## Slide 31: Compute Shader
Throw all of the existing stages out
Just use the GPU as a compute device
Now common for neural nets & other task
Eventually, we may write entire pipelines
  But for now, the standard stages are useful
COMP 5812M: Foundations of Modelling & Rendering

## Slide 32: Images by
S3: Nana Dua
S7: Mae Um
S22: Umberto
S27: Lance Grandahl